## Slide 1
COMPSCI 412
Intro. of Computer Organization
Haijian Sun
Email: sunh@uww.edu

## Slide 2: Class Overview

## Slide 3: Computer Organization
Computer
Notes: you may have seen the inside of a computer.

## Slide 4: Learning Object (Processors)
The organization of a simple computer with one CPU and two I/O devices.
History of Computer
Notes: register is temp storage for middle outputs and command.

## Slide 5: 1st Generation Computer
Organization is how features are implemented
  Like body
The 1st Generation
  Vacuum Tubes
  ENIAC (20,000 vacuum tubes)
  Decimal (not binary)
  Programmed manually by switches
Notes: 7200 crytal diodes
Decimal (not binary)
  10 vacuum tubes represented each digit
  Only one was on to represent one of 10 numbers
  Programmer change the switches and line to make a program.

## Slide 6: Stored Program concept
It was tedious to program ENIAC manually
  Why not store the commands in the memory and let the computer read them?
  Main memory storing programs and data
  ALU (Arithmetic and Logic Unit) operating on binary data
  Control unit interpreting instructions from memory and executing
  Input & output equipment operated by control unit
Notes: make more components: Main memory, ALU and control Unit
ALU process binary data.

## Slide 7: IAS Computer
John von Neumann and colleagues began design of IAS (Institute for Advanced Study) Computer.
  Completed in 1952
Mother of all subsequent general purpose computer
Notes: It is the mother of all subsequent general purpose computer.

## Slide 8: 2nd generation
Transistors
  Invented 1947 at Bell Labs by William Shockley et al. (Nobel prize in Physics in 1956)
Replaced vacuum tubes
Transistors are
  Smaller, Cheaper, Less heat dissipation
  Solid State device. No need for wires, metal plates, glass capsule. Made from Silicon (Sand)

## Slide 9: 3rd Generation
Until early 1960s, computers were composed of discrete components (transistors, resistors, capacitors, etc), manufactured separately.
  Transistor  circuit board: expensive
  Early 2nd gen: 10,000 transistors.
  Later needed 100,000.
  How to put them all?
Integrated Circuit
  Birth of Microelectronics
Notes: However, more transistors required for the computer to make better performance.

## Slide 10: Intel Processors
4-bit Processors
  4004, 4040
  First microprocessor
  All CPU components on a single chip
8-bit Processors
  8008,8080,8065
    Intel’s 1st general purpose microprocessor
16-bit Processors
  8086, 8088, 80186, 80286
  80186: Assembly Language compatible
  80286: Embedded, 16 Mbyte memory addressable
Notes: 4-bit processor is the first 3rd generation cpu.

## Slide 11: War on 64-bit standard
Increase bit for improving Processors
  Until 32-bit processor
64-bit processor is not an extension of 32-bit
  Completely different
  new instructions set from 32-bit processor
  Mostly for servers
AMD announced 64 bits architecture (AMD64 or x86-64), 2003
    Long mode (extends all IA-32 instructions to 64 bit)
    Legacy mode (identical to IA-32)
    Compatibility mode (user pg in IA-32, OS in AMD64)
Notes: However, after 32 bit processor, the 64 bit processor is required new architecture for the processor.
IA-64 is the instruction set architecture (ISA) of the Itanium family of 64-bit Intel microprocessors

## Slide 12: War on 64-bit standard
IA-64 is not an extension of IA-32
  Completely different
  New instructions set from IA-32
  Mostly for servers
AMD announced 64 bits architecture (AMD64 or x86-64), 2003
    Long mode (extends all IA-32 instructions to 64 bit)
    Legacy mode (identical to IA-32)
    Compatibility mode (user pg in IA-32, OS in AMD64)
Intel embraces AMD64 IA-32e (EM64T, and now Intel 64), 2004
Notes: However, after 32 bit processor, the 64 bit processor is required new architecture for the processor.

## Slide 13: Increasing Speed of Processor
Three Strategies to Improve CPU performance
  Increase hardware speed of processor
    By shrinking logic gate size
      More gates packed more tightly
         Propagation time for signals reduced
    By increasing clock rate
Notes: We briefly showed the history of computer and CPU

## Slide 14: Increasing Speed of Processor
Problems with strategy 1
  Power
    Power density (Watts/cm2) increases with density of logic and clock speed
    Dissipate more heat  The greatest problem now
  RC delay (Resistance, Capacitance)
    Wire interconnects thinner, increasing resistance
    Wires closer together, increasing capacitance
    RC product increases  delay increases
  Memory latency
    Memory speeds lag processor speeds
  Better Solution:
    More emphasis on organizational and architectural

## Slide 15: Increasing Speed of Processor
Increase size and speed of caches
  And dedicate a part of processor chip
   cache access times drop significantly
Change processor organization and architecture
  Increase effective speed of execution
  With some kind of parallelism
Notes: We briefly showed the history of computer and CPU

## Slide 16: Graphics Processing Unit (GPU)
Perform parallel operations on graphics data
  Used to encode and render 2D and 3D graphics as well as process video
  Coined by NVIDIA in 1999 (GeForce) – drawing polygon without CPU’s help – good for games!
  OpenCL (Standard = Intel, AMD…), CUDA (Nvidia)
  Ideal for deep learning, AI, autonomous cars
Notes: Designed to perform parallel operations on graphics data
  Traditionally found on a plug-in graphics card, used to encode and render 2D and 3D graphics as well as process video
  Coined by NVIDIA in 1999 (GeForce) – drawing polygon without CPU’s help – good for games!
General Purpose Computing on GPU (GPGPU)
  Broad ranges of applications are supported (> CPU, ~2005)
  OpenCL (Standard = Intel, AMD…), CUDA (Nvidia)
  Ideal for deep learning, AI, autonomous cars

## Slide 17: CPU + GPU = APU
Accelerated Processor Unit (by AMD) (2010)
  Using the same bus
  Lower cost, lower power consumption
  Mediocre performance, low market share  Big failure  caused the demise of AMD
  Later adopted by video game machines by Sony (Playstation 4) and MS (Xbox 1) (2013)
Intel HD Graphics
  Sandy Bridge (2011)

## Slide 18: Summary
Modern Computer
  Main memory storing programs and data
  ALU (Arithmetic and Logic Unit) operating on binary data
  Control unit interpreting instructions from memory and executing
  Input & output equipment operated by control unit
Increase CPU performance
  Increase hardware speed of processor
  Increase size and speed of caches
  Change processor organization and architecture