## Slide 1
CPU Register Design (Load & Store)
Haijian Sun
sunh@uww.edu
Notes: http://mr-g.tistory.com/60
you are the great programmer who knows not only a programming language but also system programming.

## Slide 2: Learning Object
CPU Register Design (Programmer’s Perspective)
  CPU Register Design
    Load & Store Design

## Slide 3: CPU Register Design
Programmer’s Perspective
  Resistor design and instruction Design
Register Design
  Number of resistor
    Let 8 resistors
  Number of bits
    Let 16-bit register
  Purpose of each resistor
    Get higher speed
    Simplify the instructions
Structure of Register
General purpose
16 bit register
Notes: Let’s make cpu design as a programmer.
I will explain how to design cpu with simple example using 16 bits register.
If we set purpose of each resistor, we get higher speed and simplify the instructions.
R0~r3 are general purpose registers for ALU operating
It is for operation and calculation

## Slide 4: LOAD & STORE Design
Limitation of Arithmetic instruction
  operand – only store number or instruction address
    Can we store main memory address on Operand? No.
  Arithmetic instruction can not operate :
    int a = 10; // Allocate 0x30 address
  Solution: New instruction to store/load data
LOAD & STORE instruction Design
  To store value in main memory address
r0
r1
r2
r3
Register
Main Memory
Store
Load
int a = 10; //allocate 0x10
int b = 20; //allocate 0x20
int c = 0; //allocate 0x30
c = a + b
Notes: All the Arithmetic operation is on the register (Limitation)
if number is bigger than16 bits, we can not save it in the register.

## Slide 5: LOAD & STORE Design – cont.
Program Developer
Hardware Engineer
I want to use Main Memory (Bigger size of Memory) to store more program and bigger number
Okay
Add main memory (8 bits address
0x00 ~ 0xFF)
Make LOAD & STORE to use main memory
Can only save 16 bits number (65536)

## Slide 6: LOAD Instruction Design
Operator (3 bits)- LOAD (110)
  Make new binary code in operator
  Change the format of instruction
Destination
  Register address (3 bits) to load data
Source
  Main memory address (8 bits) to read data
  E.g. LOAD r3, 0x07
Reservation
LOAD
Destination
Source
Symbol | Binary
ADD | 001
SUB | 010
MUL | 011
DIV | 100
LOAD | 110
New Format
Notes: we make new binary code in operator
Load 0x07’s data to r3

## Slide 7: STORE Instruction Design
Operator (3 bits)- STORE (111)
  Make new binary code in operator
  Change the format of instruction
Source
  Register address (3 bits) to read data
Destination
  Main memory address (8 bits) to store data
  E.g. STORE r2, 0x08
Reservation
STORE
Source
Destination
Symbol | Binary
ADD | 001
SUB | 010
MUL | 011
DIV | 100
LOAD | 110
STORE | 111
New Format
Notes: Store r2’s data into 0x08

## Slide 8: Example
In program
  int a = 30; //allocate 0x10
  int b = 40; //allocate 0x20
  int c = a + b; //allocate 0x30
Change to Assembly
  LOAD r1, 0x10
  LOAD r2, 0x20
  ADD r3, r1, r2
  STORE r3, 0x30
0
0
1
1
0
0
0
1
0
0
0
1
0
0
0
0
Symbol | Binary
r0 | 000
r1 | 001
r2 | 010
r3 | 011
Symbol | Binary
ADD | 001
SUB | 010
MUL | 011
DIV | 100
LOAD | 110
STORE | 111
0
0
1
1
0
0
1
0
0
0
1
0
0
0
0
0
0
0
0
0
1
0
1
1
1
0
0
1
1
0
1
0
0
0
1
1
1
0
1
1
0
0
1
1
0
0
0
0

## Slide 9: Practice 1
In program
  int a = 100; //allocate 0x20
  int b = a - 1; //allocate 0x30
Change to Assembly
  LOAD r3, 0x20
  SUB r0, r3, 1
  STORE r0, 0x30
Fill in the blank =>
0
0
0
0
1
0
0
0
0
0
Symbol | Binary
r0 | 000
r1 | 001
r2 | 010
r3 | 011
Symbol | Binary
ADD | 001
SUB | 010
MUL | 011
DIV | 100
LOAD | 110
STORE | 111
0
0
0
0
0
0
1
1
0
0
0
0

## Slide 10: Practice 2
In program
  int a = 100; //allocate 0x10
  int b = a - 1; //allocate 0x20
  int c = a*b; //allocate 0x30
Change to assembly
Change to instructions (binary code)
Symbol | Binary
r0 | 000
r1 | 001
r2 | 010
r3 | 011
Symbol | Binary
ADD | 001
SUB | 010
MUL | 011
DIV | 100
LOAD | 110
STORE | 111

## Slide 11: Program Flow (LOAD & STORE)
int a = 30; //allocate 0x10
int b = 40; //allocate 0x20
int c = a + b
LOAD r1, 0x10
LOAD r2, 0x20
ADD r3, r1, r2
STORE r3, 0x30
Memory
ALU
Control Unit
I/O BUS
CPU
1. Compile
5. Decode
6. Execution
r0
r1
r2
r3
r4 ir
r5 sp
r6 lr
r7 pc
00…
00..
00..
00..
2. Assemble
3. LOAD
4. Fetch
30
40
0
…
…
…
…
10
20
30
30
10
20
30
Memory Address
Memory Address
Value
Value

## Slide 12: Summary
LOAD & STORE instruction Design
  To store value in main memory address
Load instruction
STORE instruction
Symbol | Binary
LOAD | 110
STORE | 111
Register Address
Main Memory Address