## Slide 1
CPU Register Design (Direct & Indirect)
Haijian Sun
sunh@uww.edu
Notes: http://mr-g.tistory.com/60
you are the great programmer who knows not only a programming language but also system programming.

## Slide 2: Learning Object
CPU Register Design (Programmer’s Perspective)
  CPU Register Design
    Direct & Indirect Mode Design

## Slide 3: Limitation of Load & Store
Limited storage (Issues on Direct Mode)
  Instruction can describe only between 0x0000 and 0x00ff in main memory
  (ff)16 = (1111 1111)2
  Can not describe over 0x0100 in main memory address
Reservation
LOAD
Destination
Source
8 bits for main memory address
LOAD instruction
0 0

## Slide 4: CPU Register Design
Program Developer
Hardware Engineer
Okay, now I want to use more memory.
Okay
Increasing size of main memory
(> 0x0100)
Current Register only manages 0x00 ~ 0xFF address.
Need another instructions.
Let’s use reservation bit

## Slide 5: Solution for Memory Limitation
Let CPU know what main memory contains
  Store address between 0x00 and 0xff
              OR
Reservation
LOAD
Destination
Source
8 bits for main memory address
LOAD instruction
Use the Reservation bit to let CPU know what is in the memory (number or address) in the Source address
Value 100
In Memory (Direct)
Address 0x100
In Memory (Indirect)

## Slide 6: Indirect Addressing Mode
Indirect Mode
  Reference the address in main memory
  Solve the issue of direct addressing mode
  E.g. LOAD r1, [0x10]
Direct Addressing
Indirect Addressing
LOAD r1, 0x10
LOAD r1, [0x10]
Notes: Using Bracket, the indirect address is displayed.

## Slide 7: How to Distinguish Modes
Reserved bit for Mode
Reserved bits (2 bits)
  Let 11 on reservation for Indirect Mode
Indirect Addressing
LOAD r1, [0x07]
Notes: How to distinguish the modes.

## Slide 8: Example Indirect Mode
int a = 10
  LOAD r1, 0x0010
  Only control register
Int b = 20 (Making Indirect)
  Need to put 0x0100 (256) between 0x00 and 0xff
  MUL r0, 4, 4
    r0 = 4 x 4
  MUL r2, 4, 4
    r2 = 4 x 4
  MUL r3, r0, r2
    r3 = r0 x r2 // Get 0x0100 (256)
int a = 10; //allocate 0x0010
int b = 20; //allocate 0x0100
int c = 0; //allocate 0x0020
c = a + b
Let the code is already on Memory
How to access?
Notes: Hexadecimal

## Slide 9: Example Indirect Mode (cont.)
Use Indirect Mode
  First we need store the address on memory
  STORE r3, 0x0030
    -> 0x0100 (main memory address)
  Load the data using Indirect Mode
  LOAD r2, [0x0030]
c = a + b
  ADD r3, r1, r2
  Store r3 0x0020
int a = 10; //allocate 0x0010
int b = 20; //allocate 0x0100
int c = 0; //allocate 0x0020
c = a + b
0x0100
0x0030
Notes: Hexadecimal

## Slide 10: Practices
Program:
  int a = 10; //allocate 0x0010
  int b = 20; //allocate 0x0200 (512)
  int c = 0; //allocate 0x0100 (256)
  c = a / b;
Assembly Code:
  Need to save 0x0200 address between 0x00 and 0xff
Let’s make binary code:
0x0200
0x0200
0x0100
0x0030
0
0x0100
Make it
Make it
Notes: LOAD r1, 0x10
  MUL r0, 4, 4
  MUL r2, r0, r0
  MUL r0, r2, 2
  STORE r0 0x0020
  STORE r2 0x0030
  LOAD r2, [0x0020]
  DIV r3, r1, r2
  STORE r3, [0x0030]

## Slide 11: Program Flow with Mode
int a = 10; //allocate 0x0010
int b = 20; //allocate 0x0100
int c = a + b //allocate 0x0020
LOAD r1, 0x10
  MUL r0, 4, 4
  MUL r2, 4, 4
  MUL r3, r0, r2
  STORE r3, 0x0030
  LOAD r2, [0x0030]
  ADD r3, r1, r2
  STORE r3, 0x20
Memory
ALU
Control Unit
I/O BUS
CPU
1. Compile
5. Decode
6. Execution
r0
r1
r2
r3
r4 ir
r5 sp
r6 lr
r7 pc
00…
00..
00..
00..
00 …
11…
00 …
2. Assemble
10
0x100
10
0x100
3. Fetch
0x0100
0x0030
Store
Indirect

## Slide 12: Program Flow with Mode
int a = 10; //allocate 0x0010
int b = 20; //allocate 0x0100
int c = a + b //allocate 0x0020
LOAD r1, 0x10
  MUL r0, 4, 4
  MUL r2, 4, 4
  MUL r3, r0, r2
  STORE r3, 0x0030
  LOAD r2, [0x0030]
  ADD r3, r1, r2
  STORE r3, 0x0020
Memory
ALU
Control Unit
I/O BUS
CPU
1. Compile
5. Decode
6. Execution
r0
r1
r2
r3
r4 ir
r5 sp
r6 lr
r7 pc
00…
00..
00..
00..
01 …
11…
00 …
2. Assemble
10
20
30
10
20
30
3. Fetch
0x0100
0x0030
LOAD

## Slide 13: Summary
Indirect Mode (11)
  Reference the address in main memory
  E.g. LOAD r1, [0x10]
Direct Addressing
Indirect Addressing
LOAD r1, 0x10
LOAD r1, [0x10]
CPU Don’t know what is in there.
(number or addr)
CPU: I got the data from the address.
CPU: Oh! first two bits is 11. So, it is not a number (data). Let move to the address.
Notes: Using Bracket, the indirect address is displayed.

## Slide 14: Summary – cont.
First, let’s make 0x0100
  MUL r0, 4, 4 4 * 4 = 16 ( r0 has 16 bits – it can store)
  MUL r2, 4, 4 4* 4 = 16 ( r2 has 16 bits – it can store)
  MUL r3, r0, r2 r0 * r2 = 256 ( r3 store the 256 (256)10 = (100)16)
Store the r3 value one of address between 0x00 and 0xff
STORE r3, 0x0030 <= 100 is saved at 0x0030 address
To use the value => LOAD r2, [0x0030]
  Use bracket give information: the 0x0030 has another memory address, not number
int a = 10; //allocate 0x0010
int b = 20; //allocate 0x0100
int c = 0; //allocate 0x0020
c = a + b
Oh, my ‘b’ variable is stored at 0x0100 in main memory.
Need to store the 0x100 in one of address between 0x00 and 0xff in main memory, because, STORE and LOAD have only 8 bits for main address.
Notes: Load and Store instruction can only access between 00 and ff.
bracket

## Slide 15: Summary and Review
int a = 10; //allocate 0x0010
int b = 20; //allocate 0x0100
int c = a + b //allocate 0x0020
LOAD r1, 0x10
  MUL r0, 4, 4
  MUL r2, 4, 4
  MUL r3, r0, r2
  STORE r3, 0x0030
  LOAD r2, [0x0030]
  ADD r3, r1, r2
  STORE r3, 0x0020
Memory
ALU
Control Unit
I/O BUS
CPU
1. Compile
5. Decode
6. Execution
r0
r1
r2
r3
r4 ir
r5 sp
r6 lr
r7 pc
00…
00..
00..
00..
00 …
11…
00 …
2. Assemble
10
20
30
10
20
30
3. Fetch
0x0100
0x0030
LOAD