## Slide 1
Procedure Call Stack (SP Register)
Haijian Sun
sunh@uww.edu

## Slide 2: Learning Object
Use More Main Memory
Notes: HW: Circuit Design

## Slide 3: Learning Object
(Preserved) Register
  ir (instruction register): next instruction which will execute
  sp (stack pointer): point current stack location
  lr (link register): return location after finishing sub function.
  pc (program counter): current program/code address
Register | Binary
r4, ir | 100
r5, sp | 101
r6, lr | 110
r7, pc | 111

## Slide 4: Current Your Computer
Basic Calculator
  +,-,/,*
  Store and Load variable on the main memory
  Large number
Now, we want to more function
  Call Function
    Parameter, variables, return
Need more function in the limited resource.
Let’s use special purpose 4 registers
Like, Basic Programming Language
More, Advanced Programming Languge

## Slide 5: Local Variable
Programming function
  Use Variables such as local variable, global variable
Stack
  Local variable is saved in stack
Stack Frame
  Memory space for local variables on a function
Stack Point (sp) register
  Point the current location on stack
SP
Notes: To use local variable in main memory we need to know the three components.

## Slide 6: Stack
Stack (Last In, Frist Out)
  Memory space for local variable
In computer science, a stack is an abstract data type that serves as a collection of elements (data), with two principal operations:
  Push (write): add an element/data to the collection
  Pop (read): removes the most recently added element/data that was not yet removed in memory

## Slide 7: Stack Frame
Stack Frame (SF)
  Memory block which is allocated memory for local variable.
  Main function’s SF
    a=1, b=2 in memory.
  fc1 function’s SF
    c=3, d=4 in memory.
  fc2 function’s SF
    e=5, h=6 in memory.
Stack Frame

## Slide 8: Stack Frame
Computer stack the element/data in memory
  How did the CPU get to know where the next location?
Save the top of stack’s address
SP Register

## Slide 9: Flow of Stack Pointer 1
Stack Pointer (SP) register
  Point next address
int main(void)
{
int a = 1;
int b = 2;
fc1();
}
int fc1(void)
{
int c = 3;
int d = 4;
fc2();
}
int fc2(void)
{
int e = 5;
int f = 6;
}
r0
r1
r2
r3
r4 ir
r5 sp
r6 lr
r7 pc
Flow of code
Start sp
Notes: How to work

## Slide 10: Flow of Stack Pointer 1
Stack Pointer (SP) register
  point next address
int main(void)
{
int a =1;
int b =2;
fc1();
}
int fc1(void)
{
int c =3;
int d =4;
fc2();
}
int fc2(void)
{
int e =6;
int f =5;
}
r0
r1
r2
r3
r4 ir
r5 sp
r6 lr
r7 pc
a = 1
Flow of code
increase sp value

## Slide 11: Flow of Stack Pointer 2
Start main function
  Stack variable a and b
int main(void)
{
int a = 1;
int b = 2;
fc1();
}
int fc1(void)
{
int c = 3;
int d = 4;
fc2();
}
int fc2(void)
{
int e = 5;
int f = 6;
}
r0
r1
r2
r3
r4 ir
r5 sp
r6 lr
r7 pc
b = 2
a = 1
Flow of code
increase sp value

## Slide 12: Flow of Stack Pointer 3
Call fc1 function from main function
  Stack variable c
int main(void)
{
int a = 1;
int b = 2;
fc1();
}
int fc1(void)
{
int c = 3;
int d = 4;
fc2();
}
int fc2(void)
{
int e = 5;
int f = 6;
}
r0
r1
r2
r3
r4 ir
r5 sp
r6 lr
r7 pc
c = 3
b = 2
a = 1
Flow of code
increase sp value

## Slide 13: Flow of Stack Pointer 4
Call fc1 function from main function
  Stack variable d
int main(void)
{
int a = 1;
int b = 2;
fc1();
}
int fc1(void)
{
int c = 3;
int d = 4;
fc2();
}
int fc2(void)
{
int e = 5;
int f = 6;
}
r0
r1
r2
r3
r4 ir
r5 sp
r6 lr
r7 pc
d = 4
c = 3
b = 2
a = 1
Flow of code
increase sp value

## Slide 14: Flow of Stack Pointer 5
Call fc2 function from fc1 function
  Stack variable d
int main(void)
{
int a = 1;
int b = 2;
fc1();
}
int fc1(void)
{
int c = 3;
int d = 4;
fc2();
}
int fc2(void)
{
int e = 5;
int f = 6;
}
r0
r1
r2
r3
r4 ir
r5 sp
r6 lr
r7 pc
e = 5
d = 4
c = 3
b = 2
a = 1
Flow of code
increase sp value

## Slide 15: Flow of Stack Pointer 6
Call fc2 function from fc1 function
  Stack variable d
int main(void)
{
int a = 1;
int b = 2;
fc1();
}
int fc1(void)
{
int c = 3;
int d = 4;
fc2();
}
int fc2(void)
{
int e = 5;
int f = 6;
}
r0
r1
r2
r3
r4 ir
r5 sp
r6 lr
r7 pc
f = 6
e = 5
d = 4
c = 3
b = 2
a = 1
Flow of code
Final SP

## Slide 16: Practices
Fill out the (green) main memory
  Show the arrow of sp register
int main(void)
{
int a = 1;
int b = 2;
fc2();
}
int fc1(void)
{
int c = 3;
int d = 4;
}
int fc2(void)
{
int e = 5;
int f = 6;
fc1();
}
r0
r1
r2
r3
r4 ir
r5 sp
r6 lr
r7 pc

## Slide 17: Summary
Stack Pointer (SP) register
  Increasing value when allocated variable (point next address)
return
  Decreasing value when function is finished
    How to know the amount memory that is released when return function
Return fc2
Return fc1
Final sp
Before call fc2
Before call fc1
Start sp
SP Register
I need backup a register for return memory.
I need backup a register for return address.