## Slide 1: Number Systems
System | Base | Symbols
Decimal | 10 | 0, 1, … 9
Binary | 2 | 0, 1
Octal | 8 | 0, 1, … 7
Hexa- decimal | 16 | 0, 1, … 9, A, B, … F

## Slide 2: Counting
Decimal | Binary | Octal | Hexa- decimal
0 | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 10 | 2 | 2
3 | 11 | 3 | 3
4 | 100 | 4 | 4
5 | 101 | 5 | 5
6 | 110 | 6 | 6
7 | 111 | 7 | 7

## Slide 3: Counting
Decimal | Binary | Octal | Hexa- decimal
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 4: Counting
Decimal | Binary | Octal | Hexa- decimal
16 | 10000 | 20 | 10
17 | 10001 | 21 | 11
18 | 10010 | 22 | 12
19 | 10011 | 23 | 13
20 | 10100 | 24 | 14
21 | 10101 | 25 | 15
22 | 10110 | 26 | 16
23 | 10111 | 27 | 17

## Slide 5: Example

## Slide 6: Decimal →Decimal
  Multiply each bit by 10n, where n is the “position” of the bit starting from 0 on the right
  Add the results
12510 => 5 x 100 = 5 2 x 101 = 20 1 x 102 = 100 125

## Slide 7: Binary →Decimal
1010112 => 1 x 20 = 1 1 x 21 = 2 0 x 22 = 0 1 x 23 = 8 0 x 24 = 0 1 x 25 = 32
4310
  Multiply each bit by 2n, where n is the “position” of the bit starting from 0 on the right
  Add the results

## Slide 8: Octal →Decimal
  Multiply each bit by 8n, where n is the “position” of the bit starting from 0 on the right
  Add the results

## Slide 9: Hexadecimal →Decimal
ABC16 => C x 160 = 12 x 1 = 12 B x 161 = 11 x 16 = 176 A x 162 = 10 x 256 = 2560
274810
  Multiply each bit by 16n, where n is the “position” of the bit starting from 0 on the right
  Add the results

## Slide 10: Decimal →Binary
12510 = ?2
Divide by 2 and keep track of the remainder
125 /2 | 62 | 1
62/2 | 31 | 0
31/2 | 15 | 1
15/2 | 7 | 1
7/2 | 3 | 1
3/2 | 1 | 1
1/2 | 0 | 1
Quotient
Remainder
12510 = 11111012

## Slide 11: Decimal →Octal
123410 = ?8
Divide by 8 and keep track of the remainder
1234/8 | 154 | 2
154/8 | 19 | 2
19/8 | 2 | 3
2/8 | 0 | 2
Quotient
Remainder
123410 = 23228

## Slide 12: Decimal →Hexadecimal
123416 = ?8
  Divide by 16 and keep track of the remainder
1234/16 | 77 | 2
77/16 | 4 | D
4/16 | 0 | 4
Quotient
Remainder
123410 = 4D216

## Slide 13: Binary →Octal
10110101112 = ?8
  Group bits in threes, starting on right
  Convert to octal digits
1 011 010 111
1 3 2 7
10110101112 = 13278

## Slide 14: Binary →Hexadecimal
10110111112 = ?16
  Group bits in fours, starting on right
  Convert to hexadecimal digits
10 1101 1111
2 D F
10110101112 = 2DF8

## Slide 15: Octal to Hexadecimal
  Use binary as an intermediary
10768 = ?16
10768 = 001 000 111 110 = 0010 0011 1110= 23E16

## Slide 16: Exercise
Decimal | Binary | Octal | Hexa- decimal
33 |  |  | 
 | 1110101 |  | 
 |  | 703 | 
 |  |  | 1AF

## Slide 17: Answers
Decimal | Binary | Octal | Hexa- decimal
33 | 100001 | 41 | 21
117 | 1110101 | 165 | 75
451 | 111000011 | 703 | 1C3
431 | 110101111 | 657 | 1AF

## Slide 18: Fractions
Decimal to decimal
3.14 => 4 x 10-2 = 0.04 1 x 10-1 = 0.1 3 x 100 = 3 3.14

## Slide 19: Fractions
Binary to decimal
10.1011 => 1 x 2-4 = 0.0625 1 x 2-3 = 0.125 0 x 2-2 = 0.0 1 x 2-1 = 0.5 0 x 20 = 0.0 1 x 21 = 2.0 2.6875

## Slide 20: Fractions- Decimal to Binary
.14579 x 2 0.29158 x 2 0.58316 x 2 1.16632 x 2 0.33264 x 2 0.66528 x 2 1.33056
etc.
3.14579 → Binary
11.001001...

## Slide 21: Binary Addition

## Slide 22: Hexadecimal Addition
carry=1
36 28 28 6A
42 45 58 4B
78 6D 80 B5
21 / 16 = 1, rem 5

## Slide 23: Signed Integers
Stored using Two’s complement notation

## Slide 24: 8-bit 2’s Complement Examples
Example #1
Example #2
Complement Digits
Add 1
5 = 00000101
-5 = 11111011

11111010
+1
Complement Digits
Add 1
-13 = 11110011
13 = 00001101

00001100
+1
Notes: Examples of the 2’s Complement Process.

## Slide 25: 8-bit Two’s Complement Examples
8-bit two’s complement | Decimal
00000111 | 7
00000110 | 6
00000101 | 5
00000100 | 4
00000011 | 3
00000010 | 2
00000001 | 1
00000000 | 0
11111111 | -1
11111110 | -2
11111101 | -3
11111100 | -4
11111011 | -5
11111010 | -6
11111001 | -7
11111000 | -8
Most significant bit (MSB) indicates positive or negative.
MSB = 0 positive
MSB=1 negative
To find the magnitude of a negative number, apply 2s complement as in the previous example 2.